DIN-Rail 3D Printer
With a HUGE 36” x 36” Build Area

Written By: TGit-Tech (02/2018)
Feel free to use: no strings attached (text content only / images respectfully referenced)
Last Updated: 2018.02.04

*** PROJECT IS INCOMPLETE – PLEASE CHECK BACK LATER ***

# INTRODUCTION

The “DIN-Rail 3D Printer” project's goal is to provide a cheap solution to very large 3D printing ability. It will use 1-Meter 35mm DIN Rails.

- The project implements
  - Z-Mobile CoreXY

- The project consists of:

- The project is Open Source and its main page Resides at: https://github.com/TGit-Tech/DIN-Rail-3D-Printer
  - Releases ( All Finalized Plans, Files and Documentation ) can be downloaded at:
  - This document ( most recent version ) can be seen at:

## Materials ($308.74)
#### Framing Hardware ( $262.28 )

Framing ( $ 258.73 )

  - (20) Steel DIN Rails 35mm W x 15mm H x 1M Length ( DN-R35HS1 ) - $49.50/10pcs = $99
    - https://www.automationdirect.com/adc/Shopping/Catalog/Enclosures_-z-_Subpanels_-z-_Thermal_Management_-z-_Lighting/Enclosure_Parts_-a-_Accessories/Internal_Component_Mounting_Accessories/DIN_Rails/DN-R35HS1

  - (1) Aluminum Build Plate ( 36” x 36” x 0.188 (3/16”) ) Mill Finish 6061 - $120.00 + $18 Shipping = $138
    - https://www.ebay.com/itm/272758454805

  - (4) Imperial 12650 Metric Threaded Rod M6-1.00x1M ( Pack of 5 ) - $15.81 + $5.92 Shipping = $21.73 ($4.35/ea)
    - https://www.amazon.com/gp/product/B001G4512Q

- Purchase Links
  - M6*30mm Link @ https://www.mcmaster.com/#standard-rounded-head-screws/=1bmfge1
    - Look for Metric STEEL Pan Head Phillips Screws priced @ M6x1mm x 30mm (50) for $6.40

- Bearings ( $3.55 )
  - (20) V-Groove Bearings, Model 603ZZ, 3x12x4mm, Wire Pulley ( 20PCS ( $0.18/ea )) - $3.55
    - Link https://www.aliexpress.com/item/20pcs-set-Professional-Bearing-set-hardware-tools-3-12-4mm-Model-603ZZ-Wire-pulley-with-V/32800396977.html

#### Printer Hardware ($10.52)

- Extrusion ( $ 10.52 )
  - E3D – V6 Long Distance 0.4mm 3D Printer Extruder ( $5.98 )
    - https://www.gearbest.com/3d-printer-parts/pp_613785.html
    - https://www.aliexpress.com/item/Wade-long-distance-V6-J-head-hotend-Extruder-with-cooling-fan-for-1-75mm-3mm-0/32809354646.html

  - MK7 MK8 i3 Extruder Aluminum Block Kit ( $4.54 )
    - https://www.gearbest.com/3d-printer-parts/pp_400612.html?wid=21
#### 3D-Prints & Fasteners ($35.94)

Below is the list of the Parts that need to be printed with a 3D-Printer in the order of assembly; so you can print them in the order shown and assemble them as they finish. Default printer settings are below; but check the per-part details below for any part-specific setting if one may exist .

- Parts were printed on an Anet A8 3D-Printer using Cura with the following settings
  - Layer Height = 0.2
  - Shell Thickness = 1.6
  - Fill Density = 100%
  - Print Speed = 60
  - Support = None

- Suggestions
  - Bed leveling is extra important with any Rack-Gear containing prints -- to ensure a fairly consistent width across the entire tab-out.
  - Use hairspray, tape or any preferred method that keeps large prints on the build plate – uneven builds will cause massive faults.
  - Parts that hold structure are PLA preferred due to its non-curling and non-flexible (brittle) attributes.
    - I've especially been impressed with iFun and PxMallion for cheap structurally sound PLA filament brands
  - Carriage parts are ABS preferred due to their flexible tension-ed slide screws but PLA should work fine.
    - eSun PLA+ filament makes a nice balance between PLA and ABS for such parts.
  - Push all stepper motors towards the drive rail before tightening -- to make a snug gear to rail connection ( reduces slop ).

QTY	Part Picture / Part Filename / Grams of Filament	Attaches / To	Fasteners / (!Per-Part!)*QTY	Est. Costs Per-Part / PLA Cost @ $15/Kg roll / www.boltdepot.com @100-lots	Total / Cost
4	Footing.stl / 244-grams / PLA preferred	N/A	N/A / Base X & Y Rails Top & Bottom / Front Right & Back Left	$3.66 Plastic	$14.64
4	Footing-FlipR.stl / 244-grams / PLA preferred	N/A	N/A / Base X & Y Rails Top & Bottom / Front Left & Back Right	$3.66 Plastic	$14.64
	Top-Corner.stl	Z-Rail / Top-Y-Rail / Top-Y-Rail-End / Top-X-Rail / Tie-Pieces	(2)#10-24 x 1” Machine Screws & Lock Nuts / #10-24 x 1” Machine Screw & Lock Nut / #10-24 x 1-1/4” Machine Screw & Nut [$0.02/ea] / #10-24 x 1-1/4” Machine Screw & Nut / #10-24 x 3/4” Machine Screw & Nut
	Top-Corner-FlipR.stl	Z-Rail / Top-Y-Rail / Top-Y-Rail-End / Tie-Pieces	(2)#10-24 x 1” Machine Screws & Lock Nuts / #10-24 x 1” Machine Screw & Lock Nut / #10-24 x 1-1/4” Machine Screw & Nut [$0.02/ea] / #10-24 x 3/4” Machine Screw & Nut
1	Gantry-Corner-YMotor.stl / 112-grams	Y-Motor / (2)Bearings / Y-DIN Rail & / X-DIN Brace Rail	(4)M3 x 16mm / (2)#4-40 x 3/4” Machine Screws [$0.02/ea] / (2)#4 Lock Washer / (2)#4 Flat Washer / (2)#4 Nut / (4)#10-24 x 1/2” Machine Screws / (4)#10-24 Nuts	$1.68 Plastic	$1.68
1	Gantry-Corner-YMotor / 112-grams			$1.68 Plastic	$1.68
1	Gantry-Corner-YPulley / 110-grams	Pulley	M5 * 25mm Machine Screw	$1.65 Plastic	$1.65
1	Gantry-Corner-YPulley / 110-grams			$1.65 Plastic	$1.65

Quick assembly reference pictures

- Settings and Details
  - PLA 1.75mm 3D Plastic Filament was used quoted below at $14.99 per 1-Kg Rolls
  - Original design was printed with an Anet A8 3D-Printer
    - Layer Height: 0.2mm
    - Fill Density: 100%
    - Print speed: 60mm/s
    - Support type: None

#### Electrical ($62.24)

- Stepper Motors ( $70.56 )
  - (8) Nema-17, 2-Phase 1.8-Deg, 3.96V, 0.9A, 4.4Ohm, 5mm Shaft, 42-Stepper Motor - $7.78/ea = $98.70
  - Optional Purchases
    - Anet Brand
      - Purchase link https://www.gearbest.com/3d-printer-parts/pp_540282.html
      - Holding Torque (Metric) - 0.34Nm, 34N.cm, 3467g.cm, 0.0346kg.m, 3.467kg.cm
      - Holding Torque (Standard) - 48oz.in, 0.25lb.ft
      - Product Weight – 0.2610kg, Size 3.5x4x4cm ( 1.38”x1.57”x1.57” )

    - SingaSong 17HS4401 w/1M cables - $38.88/5pcs - $7.78/ea = $62.24
      - https://www.aliexpress.com/item/5pcs-4-lead-Nema17-Stepper-Motor-42-motor-Nema-17-motor-42BYGH-40MM-1-7A-17HS4401/32376023464.html
      - 2-Phase, 1.8-Deg, 3.8V, 1.7A, 1.5Ohm, 4.2mH
      - Holding Torque (Metric) – .40Nm, 40N.cm, 4000g.cm
      - Length – 40mm, Weight - 280g

Electronics ( $70.56 )

# Assembly

Top-Corner must be bolted to Rail BEFORE the threaded rod is installed! ( Actually rod will push out of the way if needed as long as the Sub-Assembly is pushed down far enough to allow the rod to bend )

Install Gantry-Corners on a Rail BEFORE tightening the bearing bolts