DIN-Rail 3D Printer
With a HUGE 36” x 36” Build Area

Written By: TGit-Tech (02/2018)
Feel free to use: no strings attached (text content only / images respectfully referenced)
Last Updated: 2018.02.04

Place Master Picture here

# INTRODUCTION

The “DIN-Rail 3D Printer” project's goal is to provide a cheap solution to very large 3D printing ability. It will use 1-Meter 35mm DIN Rails.

- The project implements

- The project consists of:

- The project is Open Source and its main page Resides at: https://github.com/TGit-Tech/DIN-Rail-3D-Printer
  - Releases ( All Finalized Plans, Files and Documentation ) can be downloaded at:
  - This document ( most recent version ) can be seen at:

#### Cost and Materials ( $343.70 )

Framing ( $ 266.73 )

  - (16) Steel DIN Rails 35mm W x 15mm H x 1M Length ( DN-R35HS1 ) - $49.50/10pcs = $99
    - https://www.automationdirect.com/adc/Shopping/Catalog/Enclosures_-z-_Subpanels_-z-_Thermal_Management_-z-_Lighting/Enclosure_Parts_-a-_Accessories/Internal_Component_Mounting_Accessories/DIN_Rails/DN-R35HS1

  - (2) Aluminum DIN Rails 35mm W x 10mm H x 1M Length ( DN-R35SAL1-2 ) - $8.00/2pcs
    - https://www.automationdirect.com/adc/Shopping/Catalog/Enclosures_-z-_Subpanels_-z-_Thermal_Management_-z-_Lighting/Enclosure_Parts_-a-_Accessories/Internal_Component_Mounting_Accessories/DIN_Rails/DN-R35SAL1-2

  - (1) Aluminum Build Plate ( 36” x 36” x 0.188 (3/16”) ) Mill Finish 6061 - $120.00 + $18 Shipping = $138
    - https://www.ebay.com/itm/272758454805

  - (4) Imperial 12650 Metric Threaded Rod M6-1.00x1M ( Pack of 5 ) - $15.81 + $5.92 Shipping = $21.73
    - https://www.amazon.com/gp/product/B001G4512Q

- Electronics ( $98.70 )
  - (10) Nema-17, 2-Phase 1.8-Deg, 3.96V, 0.9A, 4.4Ohm, 5mm Shaft, 42-Stepper Motor - $9.87/ea = $98.70
    - Holding Torque - 0.34Nm, 48oz.in, 0.25lb.ft, 34N.cm, 3467g.cm, 0.0346kg.m, 3.467kg.cm
    - Product Weight – 0.2610kg, Size 3.5x4x4cm ( 1.38”x1.57”x1.57” )
    - https://www.gearbest.com/3d-printer-parts/pp_540282.html